Field	Value
Document Number	TL-KRC3006-02
Companion Test Plan	TP-KRC3006-02
Revision	B
Date	2026-03-29
Board Serial / ID
Tester

Record all test results in the tables below. Write PASS or FAIL in the Result column. For any FAIL result, record details in the Notes column including the measured value and the nature of the failure. Attach photographs of defects where practical.
Phase 1 — Bare Board Inspection and Testing
Visual Inspection
Step	Description	Result	Notes
1.1	Board outline and dimensions (22 x 80 mm +/- 0.2 mm)
1.2	Remove edge burrs
1.3	Audio jack cutout geometry
1.4	Through-holes (J1, J2, J3, J4, J5)
1.5	Front copper traces (F.Cu)
1.6	Back copper traces (B.Cu)
1.7	Front silkscreen legibility and correctness
1.8	Back silkscreen legibility and correctness
1.9	Solder mask coverage and alignment

Bare Board Electrical — Pass-Through Continuity (J1 to J2)
DMM continuity mode. Measure pad-to-pad on bare board. Accept: < 1 ohm.
Step	DIN Pin	Signal	Measured	Result	Notes
1.10a	1	REQ H
1.10b	2	GND
1.10c	3	B.U.
1.10d	4	ON
1.10e	5	MUTE
1.10f	6	D. GND
1.10g	7	RESET
1.10h	9	REQ C
1.10i	10	DATA C
1.10j	11	DATA H
1.10k	13	CLK

Bare Board Electrical — J3 Test Header Continuity (J1 to J3)
DMM continuity mode. Measure J3 pad to corresponding J1 pad. Accept: < 1 ohm.
Step	J3 Pin	Signal	Measured	Result	Notes
1.11a	1	GND
1.11b	2	ON
1.11c	3	B.U.
1.11d	4	RESET
1.11e	5	D. GND
1.11f	6	REQ H
1.11g	7	REQ C
1.11h	8	MUTE
1.11i	9	DATA C
1.11j	10	DATA H
1.11k	11	CLK

Bare Board Electrical — Audio Path Continuity
DMM continuity mode. Accept: < 1 ohm.
Step	From	To	Measured	Result	Notes
1.12a	J1 Pin 8 (R CH)	J4 Tip pad
1.12b	J1 Pin 12 (L CH)	J4 Ring pad
1.12c	J1 Pin 2 (GND)	J4 Sleeve pad
1.13a	J2 Pin 8 (R CH)	J5 Tip pad
1.13b	J2 Pin 12 (L CH)	J5 Ring pad
1.13c	J2 Pin 2 (GND)	J5 Sleeve pad

Bare Board Electrical — Isolation
DMM resistance mode. Accept: > 1 M ohm (open circuit).
Step	Between	And	Measured	Result	Notes
1.14a	J4 Tip pad	J5 Tip pad
1.14b	J4 Ring pad	J5 Ring pad
1.15a	B.U. (Pin 3)	GND (Pin 2)
1.15b	B.U. (Pin 3)	ON (Pin 4)
1.15c	B.U. (J3 Pin 3)	J3 Pin 2 (adjacent)
1.15d	B.U. (J3 Pin 3)	J3 Pin 4 (adjacent)
1.16a	Spot check 1:
1.16b	Spot check 2:
1.16c	Spot check 3:
1.16d	Spot check 4:
1.16e	Spot check 5:

Phase 1 Result
Phase 1 Overall Result	Date	Tester Initials	Notes

Phase 2 — Assembly and Workmanship
Workmanship Inspection
Step	Description	Result	Notes
2.1	J3 solder joints (11 pins)
2.2	J4 and J5 solder joints and seating
2.3	J1 solder joints (13 signal pins + lugs)
2.4	J2 solder joints (back side, 13 signal pins + lugs)
2.5	Post-solder cleaning (flux removal)
2.6	Final visual inspection

Phase 2 Result
Phase 2 Overall Result	Date	Tester Initials	Notes

Phase 3 — Final Electrical Verification
End-to-End Continuity
DMM continuity mode. Measure with connectors/cables inserted. Accept: < 2 ohm.
Step	Path	Measured	Result	Notes
3.1a	Cable Pin 1 (REQ H) through J1-J2 to J2 Pin 1
3.1b	Cable Pin 2 (GND) through J1-J2 to J2 Pin 2
3.1c	Cable Pin 3 (B.U.) through J1-J2 to J2 Pin 3
3.1d	Cable Pin 4 (ON) through J1-J2 to J2 Pin 4
3.1e	Cable Pin 5 (MUTE) through J1-J2 to J2 Pin 5
3.1f	Cable Pin 6 (D. GND) through J1-J2 to J2 Pin 6
3.1g	Cable Pin 7 (RESET) through J1-J2 to J2 Pin 7
3.1h	Cable Pin 9 (REQ C) through J1-J2 to J2 Pin 9
3.1i	Cable Pin 10 (DATA C) through J1-J2 to J2 Pin 10
3.1j	Cable Pin 11 (DATA H) through J1-J2 to J2 Pin 11
3.1k	Cable Pin 13 (CLK) through J1-J2 to J2 Pin 13

J3 Test Header End-to-End
With cable in J1, insert jumper wire into each J3 socket. Accept: < 2 ohm.
Step	J3 Pin / Signal	Measured	Result	Notes
3.2a	J3:1 -> J1:2
3.2b	J3:2 -> J1:4
3.2c	J3:3 -> J1:3
3.2d	J3:4 -> J1:7
3.2e	J3:5 -> J1:6
3.2f	J3:6 -> J1:1
3.2g	J3:7 -> J1:9
3.2h	J3:8 -> J1:5
3.2i	J3:9 -> J1:10
3.2j	J3:10 -> J1:11
3.2k	J3:11 -> J1:13

Audio Path End-to-End
With cables in J1/J2 and 3.5 mm plugs in J4/J5. Accept: < 2 ohm.
Step	Path	Measured	Result	Notes
3.3a	J1:8 -> J4:Tip (R CH)
3.3b	J1:12 -> J4:Ring (L CH)
3.3c	J1:2 -> J4:Sleeve (GND)
3.4a	J2:8 -> J5:Tip (R CH)
3.4b	J2:12 -> J5:Ring (L CH)
3.4c	J2:2 -> J5:Sleeve (GND)

Audio Isolation and Jumper Verification
Step	Test	Measured	Result	Notes
3.5a	J4 Tip to J5 Tip — NO cable (expect open)
3.5b	J4 Ring to J5 Ring — NO cable (expect open)
3.5c	J4 Tip to J5 Tip — WITH 3.5mm cable (expect < 2 ohm)
3.5d	J4 Ring to J5 Ring — WITH 3.5mm cable (expect < 2 ohm)

Phase 3 Result
Phase 3 Overall Result	Date	Tester Initials	Notes

Final Acceptance
	Result	Date	Initials
Phase 1 — Bare Board
Phase 2 — Assembly
Phase 3 — Final Verification
BOARD ACCEPTED FOR TP-KRC3006-01

Defect Log (attach additional pages if needed):
Defect #	Step	Description	Disposition (rework / accept / scrap)	Verified By
1
2
3
4
5

Revision History
Rev	Date	Author	Description
A	2026-03-14	Allen	Initial release.
B	2026-03-29	A. Kreager	Add step to remove burrs
C	2026-04-01	A. Kreager	Formatting. Corrected 1.11 signal names.